## Slide 1: Watershed Academy Watershed Coordinator Training Series
Dealing with Data
3. Using USGS StreamStats

## Slide 2: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: This is the homescreen when you go to the web address at the top.
You have the option of zooming in to your location, searching for a place and then zooming there, or changing the map layers.
Here we will search for Springfield Kentucky and zoom to the site.

## Slide 3: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: Here we are at Springfield, KY.
The software needs us to confirm that we are selecting Kentucky as our state. When we do that, if we are zoomed in far enough the stream lines will become big and blocky.
So we will click “Kentucky” and then change our basemap to aerial so we can navigate right to one of our sites.

## Slide 4: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: So now you can see the aerial images and the button is available to delineate the drainage area of a site if we click “Delineate” and then click on top of the blue line at the location of our site.
So we click here.

## Slide 5: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: The program delineates the area for us, as shown in the yellow.
On the way, the program warns us that there is potential karst in the area. Karst drainage can lose drainage to watershed through underground conduits.
It should be noted that this delineation is based sololy on the topography. If you have a lot of impervious surfaces and stormwater pipes make sure the outfall drainages are delineated or else results will be inaccurate.
You can see on the left side, we have the option to:
Clear the basin and try again (sometimes if you do not click directly on the stream but beside it, only a small area is delineated.
Edit the basin (you can adjust the delineation if you know the drainage has changed [advanced user])
download the shapefile (which we can then use in ArcGIS or Google Earth)
Continue

## Slide 6: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: If you click “continue” you can select different statistics and it will predict the stream flows under different conditions – low flow, peak flow, etc. Select as many as you want. And press “Continue” and you can build a report.
You can also hit the drop down arrow next to “Basin Characteristics” and you can choose what information you want in the report. We will do that.

## Slide 7: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: Here you can see that you have the option to pick:
drainage area,
elevation,
two flow variability indices,
the latitude of the outlet, and
Two measures of impervious area

## Slide 8: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: By clicking continue, it immediately gives you feedback on the basin characteristics.
If you scroll down and hit “continue” it will build a report.

## Slide 9: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: Here is the report which you can download. You can see that it shows the area, provides the basin characteristics as well as other information

## Slide 10: USGS StreamStats
https://streamstats.usgs.gov/ss/
Notes: Scrolling down you can see that this area has karst.
It then gives you the flow statistics and some information about how they were used to calculate the stats.
This is an easy to use tool that provides a lot of information quickly.
Hopefully, this will encourage you to add it to your toolbox.